# Structure of a .geo file
A .geo file contains a model's vertices and indices in a binary format. The layout is as follows:
- An unsigned short (H) signifying the number of vertices.
- An unsigned short (H) signifying the number of faces.
- For every vertex:
  - An unsigned short (H) containing the number of vertex groups. This should be, at a maximum, 4.
  - Three floats (fff) containing the position of the vertex.
  - Three floats (fff) containing the normal of the vertex.
  - Two floats (ff) containing the primary set of UV coordinates.
  - Two floats (ff) containing the secondary set of UV coordinates.
  - For every vertex group (maximum four):
    - An unsigned short (H) containing the vertex group index.
    - A float (f) containing the vertex group weight.
  - An unsigned short (H) containing the material index.
- For every face:
  - Three unsigned shorts (HHH) containing the face's indices.